<Dedication and Location of Church>
Inspection Schedule for <year>
Inspection:	Qtr 1	Qtr 2	Qtr 3	Qtr 4
Carried out on:	<date>	<date>	<date>	<date>

Bell Frame
Tighten tie bolts (wood frame)
Check for deterioration (wood frame)
Check for rust (metal frame)
Check anchoring into tower walls
Check bonding of lightning conductor (metal frame) (This should also be included in the contractors inspection of the lightning protection system in the tower)

Headstocks
Check for deterioration of wood and metalwork (wood headstock)
Check for rust (metal headstock)
Check tightness of bell nuts
Check tightness of gudgeon plate bolts (wood headstock)
Check tightness of gudgeons (metal headstocks)
Check bell hanging true on headstock (bell with canons on wood headstock)

Wheels
Check tightness of all fastenings
Check wheel is running true
Check wheel stays for damage
Check shroud, sole, bobbins and garter holes for wear or damage.

Stays and Sliders
Check tightness of stay bolts
Check for signs of incipient cracking on stay
Check slider moving freely, clean if necessary
Check for wear on slider and runner board
Check dingler is secure and moving freely (Hastings stay)
Check for signs of uneven wear on quadrant (Hastings stay)

Clappers
Check for smooth movement
Check tightness of nut on crown staple bolt, also split pin if required
Check vertical and horizontal (clapper roll) movement of clapper
Lubricate clapper bush
Check wear on clapper ball
Check attachment bolts (wooden shafted clapper)

Bearings
Lubricate plain bearings; clean excess lubricant
Check gudgeon for scoring (plain bearing)
Check tightness of bearing hold-down bolts
Check for unusual noise (ball bearing)
Check seals (ball bearing)
Check side clearance (ball bearing)

Rope Routes
Check mounting of roller boxes
Check for rope wear on roller boxes
Check rollers spinning freely and quietly
Check for wear on rollers
Check ceiling and rope guide bosses for wear or looseness.

Ropes
Check wear at garter hole on wheel
Check wear on tail end
Check for wear on sally if it passes through a rope guide or boss
Check cord on spider (if present)
Check free-running of spider pulleys (if present)

Bells
Check wear on soundbow
Check correct operation of all chiming hammers
Check clearance when chiming hammers pulled off
Check operation of Ellacombe frame (if present)
Check cables to chiming hammers and pull off

General
Check access and locks (update list of key holders): doors, stairs, trapdoors, ladders
Check lighting and power supplies throughout tower
Test emergency lighting
Tests of portable electrical appliances
Check fire extinguisher tests
Check tower roof drainage
Check generally for water ingress
Check for ingress of birds and vermin
Check windows, louvres, netting / mesh
Clean bell chamber
Clean and tidy ringing room
Clean intermediate spaces, stairs
Remove rubbish generally (N.B. items of church property may require a faculty for removal and / or disposal)
Check simulator and sensors (if present)
Check teaching aids are up to date
Check information for ringers is up to date
Check information about ringing for church visitors is up to date
Refresh information on ringer’s notice boards

Names of people carrying out checks: / <insert names>